## Slide 1
GPUs: From Graphics to AI
Part 1: Why a GPU Is Not a CPU
Hardware Description Languages
Notes: Session 1 of 3. Today: what makes a GPU different from a CPU, and how a chip built to draw triangles turned into the main engine of modern AI. Session 2 is CUDA programming. Session 3 is the AI architecture itself, built up in SystemVerilog.

## Slide 2
Three Sessions
Part 1 CPU versus GPU, and how the GPU evolved
Part 2 Programming the GPU with CUDA C++
and the libraries built on top of it
Part 3 The GPU as an AI architecture
MAC units and systolic arrays in SystemVerilog
Notes: Lay out the road map. Each session ends with an exercise. The thread that ties them together: a GPU is a design decision about where to spend transistors, and you can express that decision in an HDL.

## Slide 3
Why Should an HDL Class Care?
GPUs are written in an HDL, just like your labs
They are among the largest chips ever built
over 200 billion transistors
Nobody draws 200 billion transistors by hand
The trick is one small module, replicated
Notes: Every GPU is RTL first: Verilog or SystemVerilog, simulated, synthesized, placed and routed. The way they reach these transistor counts is the same thing students do with a generate loop: design a small processing element well, then instantiate it thousands of times.

## Slide 4
Two Ways to Be Fast
Latency: how long does one task take?
measured in seconds per task
Throughput: how many tasks finish per second?
measured in tasks per second
A CPU is built for latency
A GPU is built for throughput
Notes: This is the single most important idea of the session. Every other difference follows from it. Ask the class: which one matters when you click a button? Which one matters when you render 8 million pixels sixty times a second?

## Slide 5
Latency and Throughput: A Hose
short → low latency
tap
CPU: short, narrow hose
First drop arrives quickly
Then only a trickle
long → higher latency
tap
wide →
high
throughput
GPU: long, wide hose
First drop takes longer, then a flood
Latency = time until the first drop comes out ( hose length )
Throughput = litres per second once it flows ( hose width )
Notes: Same water pressure, two hoses. Latency is how long it takes the first drop to travel the length of the hose: the CPU's short hose wins. Throughput is how much water comes out per second once it is flowing: the GPU's wide hose wins by far. Ask which bucket fills first if you only need a cup (the CPU), and which if you need a swimming pool (the GPU). Tie it to the hardware: the GPU's long hose is the deep pipeline and memory latency it tolerates, the width is thousands of lanes and a very wide memory bus. Making the hose wider does nothing for latency, and making it shorter does little for throughput.

## Slide 6
Car or Bus?
Sports car
2 people
Bus
60 people
Trip: 10 minutes
Moves 12 people / hour
Trip: 30 minutes
Moves 120 people / hour
low latency = CPU
high throughput = GPU
Neither is faster. They are fast at different things.
Notes: Work the arithmetic on the board. The car makes 6 round trips an hour carrying 2 each way, call it 12 people. The bus is three times slower per trip but moves ten times as many people. If you are the one person in a hurry, take the car. If you have to move a stadium, take buses.

## Slide 7
Where a CPU Spends Transistors
A few large, smart cores
Big caches so data is usually close
Branch prediction: guess which way an if goes
Out-of-order execution: run whatever is ready
All of it exists to make one thread finish sooner
Notes: Most of a CPU core is not arithmetic. It is machinery that predicts, reorders and caches so that a single sequential instruction stream never waits. That machinery is expensive in area and power.

## Slide 8
Same Silicon, Different Priorities
CPU
Control
ALU
ALU
ALU
ALU
Cache
DRAM
GPU
DRAM ( much faster )
Amber = control Blue = cache Green = arithmetic
Notes: This is the classic picture from the CUDA programming guide, redrawn. It is not to scale, but the proportions are honest: the CPU spends its area on control and cache, the GPU spends it on arithmetic and gives each small group of ALUs only a sliver of control and cache.

## Slide 9
Where a GPU Spends Transistors
Thousands of small, simple arithmetic units
Little control per unit:
many units share one instruction decoder
Small caches per unit
A very wide path to memory
Notes: The GPU bets that the program has a huge amount of independent work. If that bet is right, simple units win: more of them fit, and each costs less power per operation. If the bet is wrong (one long serial chain), the GPU is slow.

## Slide 10
Memory Is Slow: The CPU Answer
A trip to DRAM costs hundreds of clock cycles
CPU strategy: avoid the wait
deep cache hierarchy L1, L2, L3
prefetch what you will probably need
speculate past the stall
Works well when the working set fits in cache
Notes: Both machines face the same physics: DRAM is far away and slow. The CPU tries hard never to wait.

## Slide 11
Memory Is Slow: The GPU Answer
GPU strategy: tolerate the wait
Keep many groups of threads resident at once
When one group stalls on memory,
switch to another group - in one clock
Every thread is slow; the machine is busy
Notes: This is latency hiding by parallelism. It needs a very large register file so that switching threads costs nothing: every resident thread keeps its registers on chip. A GPU's register file is larger than a CPU core's L1 cache.

## Slide 12
Hiding Latency With Threads
CPU thread
run
stall on memory
run
stall
GPU: four groups of threads take turns
group 0
run
waiting
run
group 1
run
waiting
run
group 2
run
waiting
run
group 3
run
waiting
ALUs busy every cycle
Each group still waits. The hardware never does.
Notes: Top row: one CPU thread alternates between useful work and stalls. Bottom: while group 0 waits, groups 1, 2 and 3 run. With enough groups the green bars tile the whole timeline. On NVIDIA hardware a group is a warp of 32 threads, which is session 2.

## Slide 13
Flynn's Taxonomy
SISD single instruction, single data
a simple CPU core
SIMD single instruction, multiple data
vector units: SSE, AVX, NEON
MISD multiple instruction, single data
a fault tolerant CPU
MIMD multiple instruction, multiple data
a multicore CPU
SIMT single instruction, multiple threads
the GPU ( NVIDIA's term )
Notes: Flynn's 1966 classification. MISD exists in the taxonomy but is rare, so leave it out. SIMT is SIMD where each lane looks like its own thread to the programmer: it has its own registers and its own index, and can even take a different branch, at a cost we will see next time.

## Slide 14
SIMD: One Decoder, Many Lanes
Instruction: ADD
a[0] b[0]
+
y[0]
a[1] b[1]
+
y[1]
a[2] b[2]
+
y[2]
a[3] b[3]
+
y[3]
a[4] b[4]
+
y[4]
a[5] b[5]
+
y[5]
a[6] b[6]
+
y[6]
a[7] b[7]
+
y[7]
Fetch and decode once. Do the work eight times.
Notes: This is the core economic idea of a GPU. Instruction fetch, decode and scheduling are paid once and amortized over every lane. Real GPUs use 32 lanes per instruction, not 8.

## Slide 15
SIMD in SystemVerilog
module simd_add #(
parameter int LANES = 8,
parameter int W = 16
) (
input logic clk, valid_in,
input logic [LANES*W-1:0] a, b,
output logic [LANES*W-1:0] y,
output logic valid_out
);
// control: built once
always_ff @(posedge clk) valid_out <= valid_in;
// datapath: replicated LANES times
for (genvar i = 0; i < LANES; i++) begin : g_lane
always_ff @(posedge clk)
if (valid_in)
y[i*W +: W] <= a[i*W +: W] + b[i*W +: W];
end
endmodule
Notes: The whole idea of the last slide in 19 lines. The valid flop is the control path and it exists once. The generate loop stamps out LANES adders. The indexed part-select a[i*W +: W] picks lane i out of the packed bus. Change LANES from 8 to 32 and the control does not grow at all.

## Slide 16
Part Select in SystemVerilog
logic [15:0] data;
logic [7:0] lower_byte;
// Selects 8 bits starting from index 8
// and going upwards (8 to 15)
assign lower_byte = data[8 +: 8];
// Equivalent to data[15:8] depending on
// declaration, or data[8:15]
Notes: The whole idea of the last slide in 19 lines. The valid flop is the control path and it exists once. The generate loop stamps out LANES adders. The indexed part-select a[i*W +: W] picks lane i out of the packed bus. Change LANES from 8 to 32 and the control does not grow at all.

## Slide 17
Part Select in SystemVerilog
module bus_splitter (
input logic [31:0] wide_bus,
output logic [7:0][3:0] split_bytes // An array of 4 bytes
);
always_comb begin
// Loop through each of the 4 byte positions
for (int i = 0; i < 4; i++) begin
// base = i * 8 (0, 8, 16, 24)
// width = 8 bits fixed
split_bytes[i] = wide_bus[(i * 8) +: 8];
end
end
endmodule
Notes: The whole idea of the last slide in 19 lines. The valid flop is the control path and it exists once. The generate loop stamps out LANES adders. The indexed part-select a[i*W +: W] picks lane i out of the packed bus. Change LANES from 8 to 32 and the control does not grow at all.

## Slide 18
SIMD in SystemVerilog
module simd_add #(
parameter int LANES = 8,
parameter int W = 16
) (
input logic clk, valid_in,
input logic [LANES*W-1:0] a, b,
output logic [LANES*W-1:0] y,
output logic valid_out
);
// control: built once
always_ff @(posedge clk) valid_out <= valid_in;
// datapath: replicated LANES times
for (genvar i = 0; i < LANES; i++) begin : g_lane
always_ff @(posedge clk)
if (valid_in)
y[i*W +: W] <= a[i*W +: W] + b[i*W +: W];
end
endmodule
Notes: The whole idea of the last slide in 19 lines. The valid flop is the control path and it exists once. The generate loop stamps out LANES adders. The indexed part-select a[i*W +: W] picks lane i out of the packed bus. Change LANES from 8 to 32 and the control does not grow at all.

## Slide 19
What the Code Tells Us
Control cost is fixed
Datapath cost grows with LANES
Double the lanes:
almost double the arithmetic
for much less than double the area
This is how a GPU scales to thousands of ALUs
Notes: Have students synthesize simd_add for LANES = 4, 8, 16, 32 in the exercise and plot the cell count. The adders dominate, and the control overhead per lane falls as 1 / LANES.

## Slide 20
Feeding the ALUs
Chart: Memory bandwidth ( TB/s )
| Server CPU 12 x DDR5-4800 | H100 HBM3 ( 2022 ) | B200 HBM3e ( 2024 ) | Rubin HBM4 ( 2026 )
Memory bandwidth ( TB/s ) | 0.46 | 3.35 | 8 | 22
Thousands of ALUs are useless if data cannot reach them
Notes: CPU figure is computed: 12 channels x 4800 MT/s x 8 bytes = 460.8 GB/s. GPU figures are vendor specifications: H100 SXM 3.35 TB/s, B200 up to 8 TB/s, Rubin 22 TB/s per NVIDIA. HBM stacks DRAM dies right next to the GPU die on a silicon interposer, with a bus thousands of bits wide. We come back to this in part 3.

## Slide 21
Which One Should Do the Work?
CPU wins
GPU wins
Long serial chains
Lots of if / else
Small data sets
Pointer chasing:
linked lists, trees
The operating system
Same operation on
millions of elements
Pixels and vertices
Matrix multiply
Neural networks
Physics, signal processing
Notes: In practice they work together. The CPU runs the program and hands the data-parallel parts to the GPU. That division of labor is exactly the host / device model of CUDA next time.

## Slide 22
How the GPU Evolved
from fixed-function graphics to AI accelerator
Notes: Now the history. Watch for the moment each feature appears, because each one was a step from graphics toward general computing.

## Slide 23
Twenty-Seven Years in One Line
1999
GeForce 256
"GPU"
2001
Programmable
shaders
2006
Unified
shaders
2007
CUDA
2012
AlexNet
2017
Tensor
Cores
2022
FP8
Transformer
Engine
2024
FP4
2026
Rubin
Graphics → general purpose → AI
Notes: One slide overview; the next sixteen slides walk through it. Point out the gap from 2007 to 2012: CUDA existed for five years before AI found it.

## Slide 24
Before the GPU
1990s 3D graphics cards were fixed-function
Hard-wired circuits for each step of drawing
texture a triangle, blend pixels, test depth
Fast, but they could do only what was wired in
Essentially a big state machine, not a processor
Notes: If you think in HDL terms: these were datapaths with configuration registers, no instruction set at all. You could set modes through the driver, but you could not program them.

## Slide 25
The Graphics Pipeline
Vertices
Transform
& Light
Rasterize
Shade
Pixels
Frame
Buffer
Millions of vertices, millions of pixels
Each one handled independently of its neighbours
A perfect fit for many simple parallel units
Notes: Green stages are the ones that later became programmable. Rasterization, turning a triangle into a list of pixels, is still mostly fixed-function today.

## Slide 26
1999: The First "GPU"
NVIDIA GeForce 256
Marketed as the first Graphics Processing Unit
Moved transform and lighting from the CPU
onto the graphics chip
Still fixed-function, but now the whole pipeline
lived on one chip
Notes: The term GPU was NVIDIA marketing, but it stuck. The technical step was taking the floating-point geometry math off the CPU.

## Slide 27
2001: Programmable Shaders
GeForce 3 and DirectX 8
A shader is a small program
run once per vertex, or once per pixel
Now the stages have an instruction set
The same program runs on every pixel:
that is SIMD
Notes: This is the moment the GPU becomes a processor. Early shaders were tiny, a few dozen instructions with no loops, but they were programs. And because the same shader runs over every pixel, the hardware is naturally SIMD.

## Slide 28
The GPGPU Hack
Early 2000s: researchers noticed the GPU
was much faster than the CPU at arithmetic
So they disguised math as graphics
arrays become textures
loop bodies become pixel shaders
results are read back as an image
It worked, but it was painful
Notes: GPGPU means general-purpose computing on GPUs. To multiply two matrices you drew a rectangle on screen and the pixel shader computed one output element per pixel. No integers, no scatter writes, limited precision. It proved the demand.

## Slide 29
2006: Unified Shaders
NVIDIA G80 ( GeForce 8800 )
Before: separate vertex units and pixel units
one kind often sat idle
After: one kind of core does every job
128 identical streaming processors
A pool of identical cores is a general computer
Notes: Load balancing drove this: some scenes are vertex-heavy, others pixel-heavy, and dedicated units waste area. Once every core is the same, nothing in the hardware is graphics-specific any more. G80 had 681 million transistors.

## Slide 30
2007: CUDA
Compute Unified Device Architecture
Program the GPU in C, with no graphics at all
Write a function, launch it on thousands of threads
Integers, pointers, arbitrary reads and writes
Session 2 is entirely about this
Notes: Announced with G80 in late 2006, public release in 2007. AMD and others later backed OpenCL; AMD now has HIP. CUDA's early lead and its libraries are a large part of why NVIDIA dominates AI today.

## Slide 31
2012: AlexNet
A deep neural network for image recognition
Trained on two gaming GPUs ( GTX 580 )
Won ImageNet 2012 by a wide margin
The lesson for the field:
deep learning works when you have enough compute
and GPUs supply it cheaply
Notes: Krizhevsky, Sutskever and Hinton. The network was split across two 3 GB cards because it would not fit on one. After 2012 nearly every serious AI result has been trained on GPUs or similar accelerators.

## Slide 32
Why Neural Networks Fit GPUs
A network layer is a matrix multiply
A matrix multiply is millions of
multiply-accumulate ( MAC ) operations
acc <= acc + a × b
Every MAC in a layer is independent
The same workload shape as shading pixels
Notes: This is why the transition happened at all. Graphics and neural networks both apply one small computation to a huge, regular array. Part 3 builds the MAC in SystemVerilog.

## Slide 33
The GPU Starts Changing for AI
2016 Pascal P100
HBM2 memory stacked beside the die
NVLink between GPUs
fast 16-bit floating point
2017 Volta V100
Tensor Cores: hardware for small matrix multiplies
Notes: From here on, new generations are designed around AI rather than games. The Tensor Core is the turning point: a functional unit whose only job is D = A x B + C on small matrix tiles. We open one up in part 3.

## Slide 34
Smaller Numbers, More Math
2020 Ampere A100
TF32 and BF16 formats, structured sparsity
  TF32: A proprietary 19-bit math mode and internal format introduced by NVIDIA for Tensor
  Bit Breakdown: Uses 1 sign bit, 8 exponent bits (matching standard FP32 range), and 10 mantissa/fraction bits (matching standard FP16 precision).
  Purpose: Acts as a drop-in replacement for standard 32-bit single-precision floating-point (FP32). It allows code written for FP32 to run much faster on Tensor Cores without any modifications, providing FP32's dynamic range with FP16's computational speed.
  BF32n: A 16-bit floating-point format originally designed by Google Brain for machine learning.
  Bit Breakdown: Uses 1 sign bit, 8 exponent bits (matching FP32 range), and 7 mantissa/fraction bits (truncated precision).
  Purpose: Replaces traditional 16-bit half-precision (FP16) in many deep learning tasks. Traditional FP16 has a narrow range and frequently overflows or underflows, requiring complex scaling techniques. BF16 keeps the same large number range as FP32, preventing overflow errors while cutting memory usage in half.
Notes: Each generation adds smaller number formats. Fewer bits per number means smaller multipliers, so more fit on the die, and less memory traffic per number. Neural networks tolerate the reduced precision surprisingly well.

## Slide 35
Smaller Numbers, More Math
2022 Hopper H100
Transformer Engine picks precision per layer
80 billion transistors
8-bit floating point ( FP8 )
Notes: Each generation adds smaller number formats. Fewer bits per number means smaller multipliers, so more fit on the die, and less memory traffic per number. Neural networks tolerate the reduced precision surprisingly well.

## Slide 36
8-bit floating point (FP8)
Purpose: It cuts the memory footprint of large language models (LLMs) and deep learning systems in half compared to 16-bit formats (like FP16 or BF16), speeding up AI training and inference.
E4M3: Uses 4 exponent bits and 3 mantissa bits (plus 1 sign bit). It offers higher precision and is ideal for forward-pass weights and activations.
E5M2: Uses 5 exponent bits and 2 mantissa bits (plus 1 sign bit). It trades precision for a much wider dynamic range, making it better suited for handling large gradient spikes during model training.
Notes: Each generation adds smaller number formats. Fewer bits per number means smaller multipliers, so more fit on the die, and less memory traffic per number. Neural networks tolerate the reduced precision surprisingly well.

## Slide 37
Today's AI GPUs
2024 Blackwell B200
two dies acting as one GPU, 208 billion transistors
4-bit floating point ( FP4 )
192 GB HBM3e at 8 TB/s
2026 Rubin
336 billion transistors, two compute dies
288 GB HBM4 at 22 TB/s
Notes: Rubin figures are from NVIDIA's Rubin platform technical blog (2026): 336B transistors, HBM4 at 22 TB/s, 288 GB per GPU, 50 PFLOPS NVFP4 inference. Two dies because a single die is limited by the reticle size of the lithography tool, about 800 square millimetres.

## Slide 38
4-bit floating point (FP4)
Bit Layout: A typical FP4 format uses 4 total bits divided into 1 sign bit, 2 exponent bits, and 1 mantissa (fraction) bit (known as E2M1).
Two-Level Scaling: Because 4 bits have very little precision on their own, formats like NVIDIA's NVFP4 use block scaling. They group 16 values together with a local FP8 scale, plus a global FP32 scale for the whole tensor.
Mixed Precision: Computation happens in fast FP4, but results accumulate in higher precision formats like FP16 or FP32 to prevent major math errors.
Notes: Each generation adds smaller number formats. Fewer bits per number means smaller multipliers, so more fit on the die, and less memory traffic per number. Neural networks tolerate the reduced precision surprisingly well.

## Slide 39
Transistors per GPU
Chart: Billions of transistors
| G80 2006 | GF110 2010 | P100 2016 | V100 2017 | A100 2020 | H100 2022 | B200 2024 | Rubin 2026
Billions of transistors | 0.681 | 3 | 15.3 | 21.1 | 54.2 | 80 | 208 | 336
About 500 times more in twenty years
Notes: GF110 is the chip in the GTX 580 that trained AlexNet. 336 / 0.681 is roughly 490. All of these were described in an HDL and verified in simulation before tape-out.

## Slide 40
What Changed, What Stayed
Stayed the same
many simple units, one instruction for many
hide memory latency with parallel threads
Changed
graphics stages → general cores
general cores → matrix engines
more bandwidth, smaller number formats
Notes: Summarize. The architectural bet from 2001 never changed: throughput over latency. What changed is what the units compute.

## Slide 41
Key Ideas from Part 1
CPU: minimize latency of one thread
GPU: maximize throughput of many threads
SIMD: pay for control once, replicate the datapath
GPUs became AI chips because neural networks
are mostly multiply-accumulate
Notes: Recap before the exercise.

## Slide 42
Let's Build a SIMD Unit
Exercise: Parameterized SIMD Adder
1. Type in simd_add and write a testbench
that drives random a, b and checks every lane
2. Synthesize for LANES = 4, 8, 16, 32
record cell count or LUTs for each
3. Plot area against LANES. What fraction is control?
4. Add a sub input that selects a + b or a − b
for all lanes at once. Where does the mux go?
Notes: Step 4 makes the point concrete: the operation select is one signal shared by every lane, which is exactly what an instruction is in SIMD. Any synthesis tool the class already uses is fine, Yosys works well for the cell counts.