## Slide 1
GPUs: From Graphics to AI
Part 2: Programming the GPU
CUDA C++ and the libraries above it
Hardware Description Languages
Notes: Session 2 of 3. Last time: why a GPU trades latency for throughput. Today: how you actually write code for it, from a first kernel up to matrix multiply, and then the libraries most people use instead of writing kernels.

## Slide 2
Review from Part 1
CPU: a few big cores, low latency
GPU: thousands of small lanes, high throughput
SIMD: one instruction drives many lanes
The GPU hides memory latency by
switching between groups of threads
Notes: Two-minute recap. Today we see those groups of threads from the programmer's side.

## Slide 3
Host and Device
Host
CPU
Device
GPU
Host memory ( DDR )
Device memory ( HBM / GDDR )
PCIe or
NVLink
Two processors, two separate memories
Data must be copied across - and that copy is slow
Notes: The vocabulary: host is the CPU and its memory, device is the GPU and its memory. A pointer from one is meaningless on the other. The PCIe link is the narrowest pipe in the picture, an order of magnitude slower than HBM, so minimizing copies is the first performance rule.

## Slide 4
Every CUDA Program
1. Allocate memory on the device
2. Copy inputs host → device
3. Launch a kernel on many threads
4. Copy results device → host
5. Free device memory
Notes: This five-step skeleton is the same in every CUDA program you will write in this class. Steps 2 and 4 are where beginners lose all their speedup.

## Slide 5
What Is a Kernel?
A function that runs on the GPU
Marked with __global__
called from the host, runs on the device
Written for one thread
The hardware runs it on thousands at once
Notes: The mental shift: you do not write the loop. You write the body of the loop for one index, and the launch supplies the indices. Other qualifiers: __device__ for functions called from GPU code, __host__ for CPU code; both together compiles twice.

## Slide 6
Grid, Block, Thread
Grid
Block (0,0)
Block (0,1)
Block (1,0)
Block (1,1)
Block (2,0)
Block (2,1)
A grid of blocks, each block a group of threads
Threads in one block can cooperate; blocks are independent
Notes: Amber boxes are threads. A block holds up to 1024 threads. Threads in a block share fast on-chip memory and can synchronize. Blocks cannot depend on each other, which lets the hardware run them in any order on any number of SMs.

## Slide 7
Who Am I?
Every thread reads built-in variables:
threadIdx my index inside the block
blockIdx my block's index in the grid
blockDim threads per block
gridDim blocks in the grid
Each has .x .y .z for 1-D, 2-D, 3-D problems
Notes: These are the only way a thread knows which piece of data it owns. They are hardware special registers, filled in at launch.

## Slide 8
From Block and Thread to i
int i = blockIdx.x * blockDim.x + threadIdx.x;
blockIdx.x = 0
0
0
1
1
2
2
3
3
blockIdx.x = 1
0
4
1
5
2
6
3
7
blockIdx.x = 2
0
8
1
9
2
10
3
11
amber = threadIdx.x green = global index i
With blockDim.x = 4: block 2, thread 1 → i = 2 · 4 + 1 = 9
Every thread gets a unique i
Notes: This one line appears in almost every 1-D kernel. It is just a mixed-radix number: block index is the high digit, thread index the low digit, base blockDim.x.

## Slide 9
Vector Add on the CPU
void vec_add(const float *a, const float *b,
float *c, int n)
{
for (int i = 0; i < n; i++)
c[i] = a[i] + b[i];
}
One thread does all n additions, one after another
Notes: The baseline. One thread walks the loop from 0 to n - 1. Ask: which iterations depend on each other? None of them. That is the signal that the loop can go to a GPU.

## Slide 10
Vector Add on the GPU
__global__
void vec_add(const float *a, const float *b,
float *c, int n)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < n)
c[i] = a[i] + b[i];
}
The loop is gone: each thread does one addition
Notes: Put the two side by side. The for loop is gone. The loop index is replaced by the computed global index. The if replaces the loop bound. The body is identical.

## Slide 11
Vortex Example:Relu
include <vx_spawn2.h> // rectified linear unit RELU
#include "common.h"
__kernel void kernel_main(kernel_arg_t* __UNIFORM__ arg) {
auto src0_ptr = reinterpret_cast<TYPE*>(arg->src0_addr);
auto dst_ptr = reinterpret_cast<TYPE*>(arg->dst_addr);
uint32_t gid = blockIdx.x * blockDim.x + threadIdx.x;
TYPE value = src0_ptr[gid];
dst_ptr[gid] = (value < 0) ? TYPE(0) : value;
}
C ommon.h:
#ifndef TYPE
#define TYPE float
#endif
typedef struct {
uint32_t num_points;
uint64_t src0_addr;
uint64_t dst_addr;
} kernel_arg_t;
Notes: Put the two side by side. The for loop is gone. The loop index is replaced by the computed global index. The if replaces the loop bound. The body is identical.

## Slide 12
Host Code: Setup
int main(void)
{
const int n = 1 << 20; // 1 M elements
size_t bytes = n * sizeof(float);
float *h_a = (float *) malloc(bytes);
float *h_b = (float *) malloc(bytes);
float *h_c = (float *) malloc(bytes);
/* ... fill h_a and h_b ... */
float *d_a, *d_b, *d_c;
cudaMalloc(&d_a, bytes);
cudaMalloc(&d_b, bytes);
cudaMalloc(&d_c, bytes);
cudaMemcpy(d_a, h_a, bytes, cudaMemcpyHostToDevice);
cudaMemcpy(d_b, h_b, bytes, cudaMemcpyHostToDevice);
Notes: Convention: h_ for host pointers, d_ for device pointers. The compiler will not stop you from dereferencing d_a on the CPU, it will just crash, so the prefix is your protection. cudaMalloc takes a pointer to the pointer because it writes the device address into it.

## Slide 13
Host Code: Launch and Clean Up
int threads = 256;
int blocks = (n + threads - 1) / threads;
vec_add<<<blocks, threads>>>(d_a, d_b, d_c, n);
cudaMemcpy(h_c, d_c, bytes, cudaMemcpyDeviceToHost);
cudaFree(d_a); cudaFree(d_b); cudaFree(d_c);
free(h_a); free(h_b); free(h_c);
return 0;
}
Notes: The triple angle brackets are the launch configuration: number of blocks, threads per block. (n + threads - 1) / threads is integer ceiling division, so there are always enough threads. The launch is asynchronous: control returns to the CPU immediately. The cudaMemcpy after it waits for the kernel to finish.

## Slide 14
Why if (i < n) ?
Blocks come in whole units of 256 threads
n = 1000:
blocks = ( 1000 + 255 ) / 256 = 4
threads = 4 × 256 = 1024
Threads 1000 .. 1023 have no element
without the check they write past the array
Notes: A classic bug: the program works for n = 1 << 20 and corrupts memory for n = 1000. The bounds check costs almost nothing.

## Slide 15
The <<< >>> Launch
kernel<<<blocks, threads>>>(args);
threads per block: a multiple of 32, at most 1024
128 or 256 is a good default
blocks: enough to cover the data
many more blocks than SMs is fine - and good
The launch returns immediately
Notes: Why a multiple of 32 becomes clear in a few slides: the hardware runs threads in warps of 32. Optional third and fourth arguments are dynamic shared memory size and a stream.

## Slide 16
Compiling: nvcc
nvcc -O2 -o vec_add vec_add.cu
vec_add.cu
host code → g++
device code → PTX
PTX → SASS ( machine code )
one executable
Notes: nvcc is a driver program. It splits the .cu file: host code goes to the system C++ compiler, device code goes to PTX, a virtual instruction set, and then ptxas turns PTX into SASS, the real machine code for a specific GPU generation. Both are packed into one executable. Keeping PTX lets the driver recompile for newer GPUs.

## Slide 17
Always Check for Errors
#define CUDA_CHECK(call) \
do { \
cudaError_t err = (call); \
if (err != cudaSuccess) { \
fprintf(stderr, "%s:%d %s\n", __FILE__, \
__LINE__, cudaGetErrorString(err)); \
exit(EXIT_FAILURE); \
} \
} while (0)
CUDA_CHECK(cudaMalloc(&d_a, bytes));
vec_add<<<blocks, threads>>>(d_a, d_b, d_c, n);
CUDA_CHECK(cudaGetLastError()); // bad launch?
CUDA_CHECK(cudaDeviceSynchronize()); // crashed?
Notes: CUDA calls fail silently: they return an error code and if you ignore it the next call fails with a confusing message. A kernel launch returns nothing, so check cudaGetLastError for configuration errors and cudaDeviceSynchronize for errors during execution. The do / while(0) wrapper makes the macro behave like one statement after an if. Same advice as the rest of the course: use the debugger, cuda-gdb and compute-sanitizer, rather than print statements.

## Slide 18
Always Check for Errors
#define CUDA_CHECK(call_xz) \ Add suffix to prevent conflicts
do { \
cudaError_t err = (call_xz); \
if (err != cudaSuccess) { \
fprintf(stderr, "%s:%d %s\n", __FILE__, \
__LINE__, cudaGetErrorString(err)); \
exit(EXIT_FAILURE); \
} \
} while (0)
CUDA_CHECK(cudaMalloc(&d_a, bytes));
vec_add<<<blocks, threads>>>(d_a, d_b, d_c, n);
CUDA_CHECK(cudaGetLastError()); // bad launch?
CUDA_CHECK(cudaDeviceSynchronize()); // crashed?
Notes: CUDA calls fail silently: they return an error code and if you ignore it the next call fails with a confusing message. A kernel launch returns nothing, so check cudaGetLastError for configuration errors and cudaDeviceSynchronize for errors during execution. The do / while(0) wrapper makes the macro behave like one statement after an if. Same advice as the rest of the course: use the debugger, cuda-gdb and compute-sanitizer, rather than print statements.

## Slide 19
Unified Memory
float *a, *b, *c;
cudaMallocManaged(&a, bytes);
cudaMallocManaged(&b, bytes);
cudaMallocManaged(&c, bytes);
for (int i = 0; i < n; i++) { // CPU writes
a[i] = 1.0f;
b[i] = 2.0f;
}
vec_add<<<blocks, threads>>>(a, b, c, n);
cudaDeviceSynchronize(); // wait for GPU
printf("%f\n", c[0]); // CPU reads
One pointer works on both sides; pages move automatically
Notes: One pointer valid on both sides. The driver migrates pages on demand. Easier to write, but you lose control of when copies happen, so it can be slower. Note the explicit cudaDeviceSynchronize: without it the CPU reads c before the kernel has finished.

## Slide 20
How the Hardware Runs It
streaming multiprocessors and warps
Notes: Now look underneath the launch. What does the hardware do with a grid of blocks?

## Slide 21
The Streaming Multiprocessor
One SM
warp scheduler
tensor core
warp scheduler
tensor core
warp scheduler
tensor core
warp scheduler
tensor core
registers + shared memory / L1
H100 has 132 SMs
Each SM:
128 FP32 lanes
4 tensor cores
up to 2048 threads
256 KB registers
Notes: The SM is the GPU's equivalent of a core. Each block is assigned to one SM and stays there. An SM can hold several blocks at once. H100 SXM numbers from NVIDIA's Hopper whitepaper: 132 SMs, 128 FP32 units per SM (16,896 total), 4 fourth-generation tensor cores per SM, 65,536 32-bit registers per SM, up to 64 warps resident. The diagram shows 4 quadrants, each with its own warp scheduler.

## Slide 22
Blocks Go to SMs
The hardware hands blocks to SMs as they free up
Small GPU: few SMs, blocks run in more rounds
Big GPU: many SMs, blocks run in fewer rounds
Same program, no recompiling
This is why blocks must be independent
Notes: This is the scalability contract of CUDA. Because you promised blocks do not depend on each other, the same binary runs on a laptop GPU with 20 SMs and a data-center GPU with 132.

## Slide 23
Warps: 32 Threads in Lockstep
A block of 128 threads = 4 warps
warp 0
warp 1
warp 2
warp 3
amber: warp 1 = threads 32 .. 63, one instruction for all
The SM issues one instruction per warp
All 32 threads execute it together: this is SIMT
Notes: The warp is the real unit of execution. Threads 0 to 31 are warp 0, 32 to 63 warp 1, and so on. This is the SIMD hardware from part 1, with 32 lanes. It is why block sizes should be multiples of 32: a block of 100 threads still occupies 4 warps, wasting 28 lanes.

## Slide 24
Branch Divergence
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (threadIdx.x % 2 == 0)
y[i] = a[i] * 2.0f; // even threads
else
y[i] = a[i] + 1.0f; // odd threads
One warp runs both paths, with half its lanes switched off each time
Notes: Inside one warp, half the threads take each branch. The hardware cannot run two different instructions in one warp at the same time, so it runs the if side with the odd lanes masked off, then the else side with the even lanes masked off. Twice the time. If the condition were blockIdx.x % 2 instead, whole warps would agree and there would be no penalty.

## Slide 25
The Memory Hierarchy
Registers
per thread
~1
Shared memory / L1
per block
~30
L2 cache
whole GPU
~200
Global memory ( HBM )
whole GPU + host copies
~500
cycles
( approx. )
Faster and smaller at the top
Notes: Latencies are order-of-magnitude figures; exact numbers vary by generation. The programmer controls registers (local variables) and shared memory (declared __shared__) directly. Shared memory is a scratchpad you manage by hand, which is the key to the tiled matrix multiply later.

## Slide 26
Coalesced Memory Access
Good: c[i]
Bad: c[i * 8]
t0
t0
t1
t1
t2
t2
t3
t3
t4
t4
t5
t5
one wide memory transaction
many transactions, most bytes wasted
Neighbouring threads should touch neighbouring addresses
The hardware merges a warp's 32 loads into a few wide ones
Notes: Memory is read in aligned segments of 32 or more bytes. If the 32 threads of a warp read 32 consecutive floats, that is 128 bytes, four 32-byte segments, very efficient. With a stride of 8 floats, each thread lands in a different segment and most of each segment is thrown away.

## Slide 27
Occupancy
Occupancy = warps resident / maximum warps
More resident warps → more to switch to
→ better latency hiding
Limited by what each thread and block uses:
registers per thread
shared memory per block
Notes: Tie back to part 1: latency hiding needs many warps to choose from. Using lots of registers per thread means fewer threads fit on the SM. Nsight Compute reports achieved occupancy. High occupancy is a means, not the goal; the goal is keeping the ALUs and memory busy.

## Slide 28
Matrix Multiply
the operation that runs modern AI
Notes: Matrix multiply is the workload that matters most for part 3. Build it up in three steps: CPU, naive GPU, tiled GPU.

## Slide 29
C = A × B
Each element of C is a dot product:
C[r][c] = Σ A[r][k] · B[k][c]
N × N matrices:
N² outputs, each needs N multiply-adds
total 2 N³ floating point operations
N = 4096: about 137 billion operations
Notes: 2 x 4096 cubed = 137.4 billion, counting the multiply and the add separately as is the convention for FLOPs. All N squared outputs are independent, so there is plenty of parallelism.

## Slide 30
Matrix Multiply on the CPU
void matmul(const float *A, const float *B,
float *C, int N)
{
for (int r = 0; r < N; r++)
for (int c = 0; c < N; c++) {
float sum = 0.0f;
for (int k = 0; k < N; k++)
sum += A[r * N + k] * B[k * N + c];
C[r * N + c] = sum;
}
}
Notes: Row-major storage: element (r, c) is at r * N + c. The outer two loops are independent; the inner k loop is a reduction. On the GPU the outer two loops disappear, just as the loop did in vector add.

## Slide 31
Naive Matrix Multiply Kernel
__global__
void matmul(const float *A, const float *B,
float *C, int N)
{
int row = blockIdx.y * blockDim.y + threadIdx.y;
int col = blockIdx.x * blockDim.x + threadIdx.x;
if (row < N && col < N) {
float sum = 0.0f;
for (int k = 0; k < N; k++)
sum += A[row * N + k] * B[k * N + col];
C[row * N + col] = sum;
}
}
Notes: One thread per output element, using 2-D indices. Notice col comes from x: consecutive threads in a warp have consecutive col, so reads of B and the write of C are coalesced. Reads of A are the same address for the whole warp, which the hardware broadcasts.

## Slide 32
A 2-D Launch
dim3 threads(16, 16); // 256 threads per block
dim3 blocks((N + 15) / 16,
(N + 15) / 16);
matmul<<<blocks, threads>>>(d_A, d_B, d_C, N);
Each block computes a 16 × 16 tile of C
Notes: dim3 is a three-component struct; unspecified components default to 1. The block covers a 16 x 16 tile of C, and the grid covers the whole matrix.

## Slide 33
What Is Wrong with the Naive Kernel?
Each thread reads a whole row of A
and a whole column of B from global memory
Every element of A is read N times
2 loads for every multiply-add:
the ALUs sit waiting on memory
Fix: reuse data from fast on-chip memory
Notes: This is the idea of arithmetic intensity, which part 3 makes formal: FLOPs per byte moved. The naive kernel does about one FLOP per 4 bytes, far too low to keep a GPU busy.

## Slide 34
Tiling
A
B
C
×
=
A block loads one tile of A and one of B into shared memory
All its threads reuse those tiles, then move to the next pair
Notes: The orange 2 x 2 tile of C needs the blue strips of A and B. Instead of every thread fetching its own copy from global memory, the block cooperatively loads a TILE x TILE chunk of each strip into shared memory, uses it TILE times, and moves along. Global traffic falls by a factor of TILE.

## Slide 35
Tiled Kernel: Setup
#define TILE 16
__global__
void matmul_tiled(const float *A, const float *B,
float *C, int N)
{
__shared__ float As[TILE][TILE]; // one tile of A
__shared__ float Bs[TILE][TILE]; // one tile of B
int tx = threadIdx.x, ty = threadIdx.y;
int row = blockIdx.y * TILE + ty;
int col = blockIdx.x * TILE + tx;
float sum = 0.0f;
Notes: The two __shared__ arrays live in the SM's on-chip shared memory and are visible to every thread in the block, unlike sum, which is a private register. row and col are the same as in the naive kernel, with TILE as the block size. Launch with dim3 threads(TILE, TILE).

## Slide 36
Tiled Kernel: The Loop
for (int t = 0; t < (N + TILE - 1) / TILE; t++) {
int ac = t * TILE + tx; // column in A
int br = t * TILE + ty; // row in B
As[ty][tx] = (row < N && ac < N) ? A[row * N + ac] : 0.0f;
Bs[ty][tx] = (br < N && col < N) ? B[br * N + col] : 0.0f;
__syncthreads();
for (int k = 0; k < TILE; k++)
sum += As[ty][k] * Bs[k][tx];
__syncthreads();
}
if (row < N && col < N)
C[row * N + col] = sum;
}
Notes: Each trip around the loop, every thread loads exactly one element of each tile, padding with zero past the edge of the matrix. Then every thread does TILE multiply-adds entirely out of shared memory. Each global value is now loaded once per tile instead of once per thread: TILE times less traffic.

## Slide 37
Why __syncthreads() Twice?
A barrier: no thread passes until all in the block arrive
First: do not compute until the tiles are fully loaded
otherwise you read stale shared memory
Second: do not load the next tile
until everyone has finished with this one
Notes: Remove either barrier and the kernel gives wrong answers, but only sometimes, which is the worst kind of bug. In HDL terms, this is a handshake: the barrier is the point where every producer has written and every consumer may read.

## Slide 38
Above CUDA
libraries and frameworks
Notes: Almost nobody writes their own matrix multiply in production. Here is what sits on top of CUDA.

## Slide 39
The Software Stack
PyTorch / JAX / TensorFlow
cuBLAS · cuDNN · CUTLASS · Triton
CUDA runtime + your kernels
Driver
GPU hardware
easier
more
control
Notes: cuBLAS is linear algebra (BLAS on the GPU), cuDNN is deep-learning primitives such as convolution and attention, CUTLASS is NVIDIA's open-source C++ template library for writing fast matrix multiplies, and Triton is a Python-embedded language for writing kernels. PyTorch calls down into all of them.

## Slide 40
cuBLAS
cuBLAS (CUDA Basic Linear Algebra Subroutines)
NVIDIA GPU-accelerated library
Implements standard basic linear algebra subprograms
Used for high-performance numerical computing / deep learning
Notes: Sgemm computes C = alpha A B + beta C in single precision. cuBLAS follows Fortran's column-major convention. A row-major matrix read as column-major is its transpose, so passing B first and A second yields the row-major product we want with no copies. Link with -lcublas. This call is typically several times faster than our tiled kernel because it uses tensor cores, register tiling and double buffering.

## Slide 41
cuDNN
cuDNN (CUDA Deep Neural Network library)
GPU-accelerated library from NVIDIA
Provides highly optimized routines for deep learning tasks
Provides building blocks (primitives) for deep neural networks
Convolution, pooling, normalization, and attention layers.
Notes: Sgemm computes C = alpha A B + beta C in single precision. cuBLAS follows Fortran's column-major convention. A row-major matrix read as column-major is its transpose, so passing B first and A second yields the row-major product we want with no copies. Link with -lcublas. This call is typically several times faster than our tiled kernel because it uses tensor cores, register tiling and double buffering.

## Slide 42
CUTLASS
CUTLASS (CUDA Templates for Linear Algebra
Subroutines and Solvers)
Open-source collection of CUDA C++ template abstractions and
Python domain-specific languages (DSLs)
Designed to implement high-performance matrix-matrix multiplication
(GEMM) and linear algebra computations on NVIDIA GPUs
Hierarchical Design: Decomposes complex linear algebra operations
into thread-block tiles, warps, and individual threads
matching the CUDA hardware model
pCuTe Library: Uses a core foundation called CuTe for defining
multidimensional tensor layouts, memory spaces, and thread
organization, simplifying complex data indexing
Mixed-Precision Support: Supports FP64, FP32, TF32, FP16, BF16,
8-bit/4-bit integers, and newer block-scaled formats
like NVFP4 and MXFP4/MXFP8
Notes: Sgemm computes C = alpha A B + beta C in single precision. cuBLAS follows Fortran's column-major convention. A row-major matrix read as column-major is its transpose, so passing B first and A second yields the row-major product we want with no copies. Link with -lcublas. This call is typically several times faster than our tiled kernel because it uses tensor cores, register tiling and double buffering.

## Slide 43
4-bit floating point (NVFP4)
Bit Layout: Uses an E2M1 configuration consisting of 1 sign bit, 2 exponent bits, and 1 mantissa bit, covering a value range of approximately -6 to 6.
Two-Level Scaling: Employs fine-grained hierarchical scaling—using an FP8 scale for local micro-blocks of 16 values and a second FP32 scale for the entire tensor—to preserve dynamic range and global distribution.
Hardware Acceleration: Designed for native execution on NVIDIA Blackwell fifth-generation Tensor Cores, allowing direct 4-bit math processing with higher-precision accumulation.
Notes: Each generation adds smaller number formats. Fewer bits per number means smaller multipliers, so more fit on the die, and less memory traffic per number. Neural networks tolerate the reduced precision surprisingly well.

## Slide 44
4-bit floating point (MXFP4)
Bit Layout: Each weight uses only 4 bits in an E2M1 layout (1 sign bit, 2 exponent bits, and 1 mantissa bit).
Block sharing: Instead of scaling every number alone, it groups 32 values into a single block
Shared scale: The whole block shares one 8-bit exponent scaling factor. This method gives small groups a wide dynamic range without wasting memory.
Notes: Each generation adds smaller number formats. Fewer bits per number means smaller multipliers, so more fit on the die, and less memory traffic per number. Neural networks tolerate the reduced precision surprisingly well.

## Slide 45
8-bit floating point (MXFP8)
Bit Layout: Values are encoded using the FP8 E4M3 format (1 sign bit, 4 exponent bits, and 3 mantissa bits).
Block Scaling: Unlike standard per-tensor FP8, MXFP8 divides tensors into contiguous blocks of 32 elements along an axis.
Shared Scaling Factors: Each 32-element block shares a single unsigned exponent-only scaling factor in the E8M0 format (8 exponent bits, 0 mantissa bits).
Granularity Benefits: Fine-grained 1x32 scaling limits the impact of data outliers to their specific local block, preventing the severe quantization noise or clipping seen in traditional 8-bit formats
Claims near-lossless 16-bit (BF16) accuracy
Notes: Each generation adds smaller number formats. Fewer bits per number means smaller multipliers, so more fit on the die, and less memory traffic per number. Neural networks tolerate the reduced precision surprisingly well.

## Slide 46
OpenAI Triton
Open-source, Python-embedded domain specific language (DSL) and compiler designed to write highly efficient custom GPU kernels.
Triton abstracts the grid of individual hardware threads into a blocked program representation—meaning operations are executed on blocks of data rather than individual scalar elements.
Operation Fusion: In standard deep learning setups, executing multiple individual functions sequentially forces data to move back and forth between the GPU's fast cache (shared memory) and its slower High Bandwidth Memory (HBM/VRAM). Triton fuses these operations into a single, unified kernel. Temporary data stays directly inside the Streaming Multiprocessor's (SM) shared memory, eliminating massive data-transfer overheads.
Automatic Hardware Optimization: The Triton compiler takes the high-level Python Abstract Syntax Tree (AST) and automatically handles low-level optimizations like memory coalescing, shared memory management, software pipelining, and scheduling within SMs.
Used by PyTorch 2.x
Notes: Sgemm computes C = alpha A B + beta C in single precision. cuBLAS follows Fortran's column-major convention. A row-major matrix read as column-major is its transpose, so passing B first and A second yields the row-major product we want with no copies. Link with -lcublas. This call is typically several times faster than our tiled kernel because it uses tensor cores, register tiling and double buffering.

## Slide 47
PyTorch
Open-source machine learning and deep learning framework
Provides a multi-dimensional array object called a Tensor that runs on GPUs and TPUs •
Autograd engine automatically calculates gradients (derivatives) required for training neural networks
Uses a dynamic graph execution style so code runs line-by-line just like standard Python
PyTorch 2.x and TorchInductor converts Python to highly optimized OpenAI Triton kernels
Notes: Sgemm computes C = alpha A B + beta C in single precision. cuBLAS follows Fortran's column-major convention. A row-major matrix read as column-major is its transpose, so passing B first and A second yields the row-major product we want with no copies. Link with -lcublas. This call is typically several times faster than our tiled kernel because it uses tensor cores, register tiling and double buffering.

## Slide 48
JAX
Open-source, high-performance low level Python library developed by Google
Designed to mimic Numerical Python (NumPy)
Adds transformations that make it incredibly fast on hardware accelerators like GPUs and TPUs.
Functional programming
Treats your code as pure mathematical functions
Low level
Notes: Sgemm computes C = alpha A B + beta C in single precision. cuBLAS follows Fortran's column-major convention. A row-major matrix read as column-major is its transpose, so passing B first and A second yields the row-major product we want with no copies. Link with -lcublas. This call is typically several times faster than our tiled kernel because it uses tensor cores, register tiling and double buffering.

## Slide 49
TensorFlow
Open-source, end-to-end machine learning platform developed by Google
Released in 2015
Python bindings
Historically dominant framework for building and training deep neural networks
TensorFlow originally relied entirely on static computation graphs
Now uses Eager execution which is dynamic but core strength remains static mapping
Notes: Sgemm computes C = alpha A B + beta C in single precision. cuBLAS follows Fortran's column-major convention. A row-major matrix read as column-major is its transpose, so passing B first and A second yields the row-major product we want with no copies. Link with -lcublas. This call is typically several times faster than our tiled kernel because it uses tensor cores, register tiling and double buffering.

## Slide 50
Calling cuBLAS
#include <cublas_v2.h>
cublasHandle_t handle;
cublasCreate(&handle);
const float alpha = 1.0f, beta = 0.0f;
// cuBLAS is column-major: ask for C^T = B^T A^T
cublasSgemm(handle, CUBLAS_OP_N, CUBLAS_OP_N,
N, N, N, &alpha,
d_B, N, d_A, N,
&beta, d_C, N);
cublasDestroy(handle);
Notes: Sgemm computes C = alpha A B + beta C in single precision. cuBLAS follows Fortran's column-major convention. A row-major matrix read as column-major is its transpose, so passing B first and A second yields the row-major product we want with no copies. Link with -lcublas. This call is typically several times faster than our tiled kernel because it uses tensor cores, register tiling and double buffering.

## Slide 51
PyTorch: One Line
import torch
a = torch.randn(4096, 4096, device="cuda")
b = torch.randn(4096, 4096, device="cuda")
c = a @ b # runs a cuBLAS kernel on the GPU
torch.cuda.synchronize() # wait, like cudaDeviceSynchronize
print(c.shape)
Same five steps as before, hidden inside the library
Notes: device=cuda allocates directly in GPU memory, the cudaMalloc step. The @ operator dispatches to cuBLAS. PyTorch launches are asynchronous too, which is why timing PyTorch code without synchronize gives nonsense numbers.

## Slide 52
Writing Kernels in Python: Triton
import triton
import triton.language as tl
@triton.jit
def add_kernel(x_ptr, y_ptr, out_ptr, n, BLOCK: tl.constexpr):
pid = tl.program_id(0) # like blockIdx.x
offs = pid * BLOCK + tl.arange(0, BLOCK)
mask = offs < n # like if (i < n)
x = tl.load(x_ptr + offs, mask=mask)
y = tl.load(y_ptr + offs, mask=mask)
tl.store(out_ptr + offs, x + y, mask=mask)
add_kernel[(triton.cdiv(n, 1024),)](x, y, out, n, BLOCK=1024)
Notes: Triton programs a whole block at once rather than one thread: tl.arange makes a vector of offsets. The compiler handles warps, coalescing and shared memory. Many PyTorch kernels are generated in Triton by torch.compile. Point out the one-to-one match with the CUDA vector add.

## Slide 53
Other Ways In
CuPy, Numba: NumPy-style arrays on the GPU
HIP: AMD's CUDA look-alike
OpenCL, SYCL: vendor-neutral standards
The model underneath is always the same:
grid → blocks → threads → warps
Notes: Learning CUDA transfers. HIP is close enough that AMD ships a tool, hipify, that translates CUDA source mechanically.

## Slide 54
Key Ideas from Part 2
Write the kernel for one thread
Index with blockIdx, blockDim, threadIdx
Warps of 32 run in lockstep: avoid divergence
Neighbours touch neighbours: coalesce
Reuse data in shared memory
In practice: call cuBLAS or PyTorch
Notes: Recap before the exercise.

## Slide 55
Let's Write Some Kernels
Exercise: Three Matrix Multiplies
1. Build vec_add and check every element against the CPU
2. Write the naive and tiled matmul kernels
3. Time each for N = 512, 1024, 2048 using cudaEvent
4. Time cublasSgemm and PyTorch a @ b at the same sizes
5. Report GFLOP/s = 2 N³ / time. Plot all four
6. Try TILE = 8, 16, 32. Explain what you see
Notes: For timing: cudaEventCreate start and stop, cudaEventRecord before and after the launch, cudaEventSynchronize(stop), cudaEventElapsedTime. Run once to warm up before timing. Expect roughly: naive slowest, tiled a few times faster, cuBLAS much faster again. TILE = 32 gives 1024 threads per block, the maximum.