## Slide 1
GPUs: From Graphics to AI
Part 3: The GPU as an AI Architecture
MAC units and systolic arrays in SystemVerilog
Hardware Description Languages
Notes: Session 3 of 3. Part 1 was why. Part 2 was how to program it. Today we open up the hardware that makes a modern GPU an AI machine, and build the key pieces ourselves in SystemVerilog.

## Slide 2
Review from Part 2
Kernels are written for one thread
Warps of 32 threads share one instruction
Matrix multiply: 2 N³ operations
Tiling reuses data from shared memory
cuBLAS was much faster than our kernel. Why?
Notes: Open with the question from the exercise. The answer is today's lecture: cuBLAS uses tensor cores, hardware our kernel never touched.

## Slide 3
A Neural Network Layer
x0
x1
x2
x3
y0
y1
y2
Every line is a weight
Each output:
weight each input
add them up
y = W x + b
A whole batch of inputs at once: Y = W X - a matrix multiply
Notes: 4 inputs, 3 outputs, 12 weights. A real layer might have 4096 inputs and 4096 outputs, 16 million weights. Process a batch of inputs together and the vector x becomes a matrix X, so the layer is exactly the matmul from last time. The nonlinearity after it is cheap by comparison.

## Slide 4
It All Comes Down to MAC
Multiply-accumulate:
acc <= acc + a × b
One layer, 4096 × 4096 weights, batch of 4096:
4096³ ≈ 69 billion MACs
A large model has hundreds of such layers
Make the MAC cheap and plentiful, and you win
Notes: 4096 cubed = 68.7 billion MACs, which is 137 billion FLOPs, the number from last session. An AI accelerator is, to first order, a machine for doing MACs and keeping them fed with data.

## Slide 5
Arithmetic Intensity
Intensity = operations / bytes moved
Vector add, FP32:
1 add per 12 bytes → 0.08 ops / byte
Matrix multiply, N × N, 16-bit:
2N³ ops per 6N² bytes → N / 3 ops / byte
N = 4096: about 1365 ops / byte
Notes: Vector add reads two floats and writes one, 12 bytes, for one add. Matmul reads two N by N matrices and writes one, 3 N squared values at 2 bytes each. Matmul reuses each value N times, which is why it can keep a GPU busy and vector add never can.

## Slide 6
The Roofline
memory
bound
compute bound
vector add
large matmul
arithmetic intensity ( ops / byte, log scale )
ops
per
second
H100 ridge point: ~ 989 TFLOP/s ÷ 3.35 TB/s ≈ 300 ops/byte
Notes: Left of the ridge, performance is limited by memory bandwidth times intensity: the red slope. Right of it, by peak arithmetic: the flat green roof. 989 TFLOP/s is H100 SXM dense BF16 tensor-core throughput from NVIDIA's datasheet. Below about 300 ops per byte, the tensor cores starve. This one picture explains both the push for more HBM bandwidth and the push for fewer bits per number.

## Slide 7
Tensor Cores
hardware built for one operation
Notes: Now the hardware. What did NVIDIA add in 2017, and why is it so much faster than the CUDA cores we used last time?

## Slide 8
CUDA Core vs Tensor Core
CUDA core
Tensor core
d = a × b + c
one scalar FMA per instruction
D = A × B + C
on 4 × 4 matrices
64 FMAs per operation ( Volta )
Same fetch, same decode, same register traffic
64 times the arithmetic
Notes: Volta's tensor core performs a 4 x 4 x 4 matrix multiply-accumulate per clock: 64 fused multiply-adds, FP16 inputs with FP16 or FP32 accumulation. V100 has 640 of them. Later generations made the tiles larger and added more formats. It is the SIMD argument from part 1 taken one step further: amortize control over a whole matrix instead of a vector.

## Slide 9
Inside One Tensor Core Operation
D
=
A
×
B
+
C
A and B: low precision ( FP16, BF16, FP8 ... )
C and D: higher precision accumulator ( FP32 )
Inside: 64 multipliers feeding adder trees
Notes: Each of the 16 outputs is a 4-term dot product plus the old value. In hardware that is 4 multipliers and an adder tree per output, 64 multipliers total. Accumulating in FP32 is what keeps low-precision training stable: the products are cheap, but the running sum keeps its precision.

## Slide 10
Number Formats
FP32
8
23
TF32
8
10
BF16
8
7
FP16
5
10
FP8 E4M3
4
3
FP4 E2M1
2
1
red = sign amber = exponent bits ( range ) green = mantissa bits ( precision )
Fewer bits: less memory, smaller multipliers
Notes: BF16 keeps FP32's 8 exponent bits, so it has the same range and only loses precision; that makes it a drop-in for training. TF32 is an internal tensor-core format on Ampere and later: FP32 range, FP16 precision. FP8 also comes in E5M2, used for gradients. FP4 E2M1 can represent only 0, 0.5, 1, 1.5, 2, 3, 4, 6 and their negatives.

## Slide 11
Why Smaller Is So Much Cheaper
An array multiplier for m-bit mantissas
has about m² partial-product cells
FP32 24 × 24 = 576
BF16 8 × 8 = 64
FP8 E4M3 4 × 4 = 16
Roughly 9 × smaller going from FP32 to BF16
Notes: Counting the hidden leading 1, an FP32 mantissa is 24 bits, BF16 is 8, E4M3 is 4. Partial products grow with the square of the width. The exponent logic is just an adder and grows linearly. So halving the width roughly quarters the multiplier, and the area saved buys more multipliers.

## Slide 12
Very Small Numbers Need a Scale
FP4 has only 16 patterns: ±0, 0.5, 1, 1.5, 2, 3, 4, 6
Real values span a much wider range
Block scaling: a small group of values
shares one scale factor
Blackwell NVFP4: every 16 values share
one 8-bit scale
Notes: Recall the biased-exponent idea from the number-representation review: range and precision are separate knobs. Block scaling moves part of the exponent out of each number and shares it across a block. NVFP4 uses 16-value blocks with an FP8 E4M3 scale, plus a per-tensor FP32 scale.

## Slide 13
The Transformer Engine
Hopper, 2022
Hardware and software that track the range
of each layer's values as training runs
Choose FP8 where it is safe,
16-bit where it is not
Scale values so they fit the small format
Notes: Named for the transformer models it targets. Blackwell's second-generation version added FP4. The point for this class: precision became a run-time decision, and the datapath supports several formats sharing the same multipliers.

## Slide 14
Build a MAC
in SystemVerilog
Notes: Enough block diagrams. Build the basic unit: a signed 8-bit multiply-accumulate with a 32-bit accumulator, the integer version of what a tensor core does.

## Slide 15
MAC Unit
a
b
×
16 bit
+
acc
register
acc
32-bit feedback
8-bit × 8-bit → 16-bit product
Accumulate in 32 bits so the sum does not overflow
Notes: The accumulator is wider than the product for the same reason a tensor core accumulates in FP32: we add many products. A 16-bit product needs 16 more bits of headroom to add 65,536 of them without overflow, which is why 32 bits is the usual choice.

## Slide 16
MAC in SystemVerilog
module mac #(
parameter int AW = 8, // input width
parameter int CW = 32 // accumulator width
) (
input logic clk, rst_n,
input logic clear, en,
input logic signed [AW-1:0] a, b,
output logic signed [CW-1:0] acc
);
logic signed [2*AW-1:0] prod;
assign prod = a * b;
always_ff @(posedge clk or negedge rst_n)
if (!rst_n) acc <= '0;
else if (clear) acc <= '0;
else if (en) acc <= acc + CW'(prod);
endmodule
Notes: Points to make: signed on every declaration, otherwise the multiply is unsigned and negative numbers break. prod is 2 * AW bits, the full product width. CW'(prod) is a size cast; because prod is signed, it sign-extends to 32 bits. clear lets us start a new dot product without a full reset.

## Slide 17
Testing the MAC
module tb_mac;
logic clk = 0, rst_n = 0, clear = 0, en = 0;
logic signed [7:0] a, b;
logic signed [31:0] acc;
int expected = 0;
mac dut (.*);
always #5 clk = ~clk;
initial begin
@(negedge clk) rst_n = 1;
repeat (100) begin
@(negedge clk);
a = $urandom; b = $urandom; en = 1;
expected += a * b;
end
@(negedge clk) en = 0;
if (acc == expected) $display("PASS acc = %0d", acc);
else $display("FAIL acc = %0d expected %0d", acc, expected);
$finish;
end
endmodule
Notes: The .* connects every port to the testbench signal of the same name. Inputs change on the falling edge so they are stable at the rising edge. The software model is one line: expected += a * b. A self-checking testbench like this is how real accelerator blocks are verified, at much larger scale.

## Slide 18
Systolic Arrays
a grid of MACs that passes data along
Notes: One MAC is not an accelerator. Now we arrange many of them so that data, once fetched, is reused by many MACs without going back to memory.

## Slide 19
What Is a Systolic Array?
A grid of identical processing elements ( PEs )
Each PE: one MAC, plus registers
Data pulses through the grid, neighbour to neighbour
like blood through the heart: systole
Each value fetched once, used by a whole row or column
Notes: H. T. Kung and Charles Leiserson, late 1970s. The idea sat mostly in textbooks until AI made matrix multiply the dominant workload. Google's first TPU (2016) is a 256 x 256 systolic array of 8-bit MACs: 65,536 of them.

## Slide 20
A 4 × 4 Systolic Array
PE
PE
PE
PE
A row 0
PE
PE
PE
PE
A row 1
PE
PE
PE
PE
A row 2
PE
PE
PE
PE
A row 3
B col 0
B col 1
B col 2
B col 3
A flows right
B flows down
Each PE keeps its own
C[r][c]
Notes: This is an output-stationary array: each PE accumulates one element of C and never moves it. Elements of A enter from the left and move one PE right per clock. Elements of B enter from the top and move one PE down per clock. Every A value is used by 4 PEs, every B value by 4 PEs, but each was fetched from memory only once.

## Slide 21
The Processing Element
module pe #(parameter int AW = 8, CW = 32) (
input logic clk, rst_n, clear,
input logic signed [AW-1:0] a_in, // from the left
input logic signed [AW-1:0] b_in, // from above
output logic signed [AW-1:0] a_out, // to the right
output logic signed [AW-1:0] b_out, // downward
output logic signed [CW-1:0] c
);
always_ff @(posedge clk or negedge rst_n)
if (!rst_n) begin
a_out <= '0; b_out <= '0; c <= '0;
end else begin
a_out <= a_in; // pass A along
b_out <= b_in; // pass B along
c <= clear ? '0 : c + a_in * b_in;
end
endmodule
Notes: It is the MAC from before plus two pipeline registers. The registers are what make it systolic: each value moves exactly one PE per clock. In c + a_in * b_in the operands are extended to the 32-bit context width before multiplying, and since all are signed the extension is a sign extension.

## Slide 22
Building the Array with generate
module systolic #(parameter int N = 4, AW = 8, CW = 32) (
input logic clk, rst_n, clear,
input logic signed [AW-1:0] a_left [N],
input logic signed [AW-1:0] b_top [N],
output logic signed [CW-1:0] c_out [N][N]
);
logic signed [AW-1:0] a_h [N][N+1]; // horizontal wires
logic signed [AW-1:0] b_v [N+1][N]; // vertical wires
for (genvar i = 0; i < N; i++) begin : g_edge
assign a_h[i][0] = a_left[i];
assign b_v[0][i] = b_top[i];
end
for (genvar r = 0; r < N; r++) begin : g_row
for (genvar c = 0; c < N; c++) begin : g_col
pe #(.AW(AW), .CW(CW)) u_pe (
.clk, .rst_n, .clear,
.a_in(a_h[r][c]), .a_out(a_h[r][c+1]),
.b_in(b_v[r][c]), .b_out(b_v[r+1][c]),
.c(c_out[r][c]));
end
end
endmodule
Notes: Two arrays of wires: a_h[r][c] is the A value entering PE (r, c) from the left, b_v[r][c] the B value entering from above. The edge loop ties the inputs to column 0 and row 0. The nested generate loop stamps out N squared PEs. Change N from 4 to 256 and you have the shape of a TPU. The last column's a_out and last row's b_out are simply unused.

## Slide 23
Feeding the Array: Skew
Row r of A enters r cycles late; column c of B enters c cycles late
cycle
0
1
2
3
4
5
6
a_left[0]
A00
A01
A02
A03
a_left[1]
A10
A11
A12
A13
a_left[2]
A20
A21
A22
A23
a_left[3]
A30
A31
A32
A33
PE ( r, c ) sees A[r][k] and B[k][c] at cycle r + c + k
Last result ready after 3N − 2 cycles
Notes: B is skewed the same way down the columns. The skew guarantees that matching pairs A[r][k] and B[k][c] arrive at PE (r, c) on the same clock: A[r][k] is delayed r cycles at the input and c cycles crossing the row; B[k][c] is delayed c at the input and r crossing the column. For N = 4 the last product reaches PE (3,3) at cycle 9 and is registered on that edge, so the full result takes 3N - 2 = 10 cycles. Pipelining the next matrix right behind this one hides most of that fill time.

## Slide 24
Output vs Weight Stationary
Output stationary ( ours )
each PE keeps one C value
A and B both move
Weight stationary ( Google TPU )
each PE holds one weight, preloaded
inputs move, partial sums move
Choose by which data you most want to reuse
Notes: Weight stationary suits inference: the weights of a layer are loaded once and millions of inputs stream through. This is a classic HDL design-space decision: it changes which registers exist and which wires are long, but the MAC is the same.

## Slide 25
Two Ways to Build an AI Chip
GPU
Systolic accelerator
Many small tensor cores
inside each SM
Surrounded by general
programmable cores
Runs graphics, HPC, AI
Flexible
One or a few huge arrays
Little general-purpose
logic
Built mostly for AI
More MACs per mm²
Notes: Both use the same building block, an array of MACs. The difference is how much general-purpose machinery surrounds it. The GPU keeps its SIMT cores so it can run any kernel, including all the non-matmul parts of a model. Dedicated accelerators such as TPUs spend nearly all their area on the array.

## Slide 26
Beyond the Core
memory and scale
Notes: Tensor cores are only half the story. The roofline told us they starve without bandwidth.

## Slide 27
High Bandwidth Memory
silicon interposer
GPU die
HBM stacks
HBM stacks
DRAM dies stacked and wired vertically, millimetres from the GPU
Very wide bus: thousands of wires instead of 64
Notes: Each stack is several DRAM dies connected by through-silicon vias, sitting on a base logic die (amber). The interposer carries thousands of short wires between stacks and GPU. HBM3 is 1024 bits wide per stack; HBM4 doubles that to 2048. Short wires mean low energy per bit. Rubin's 22 TB/s comes from HBM4. Compare a DDR5 DIMM channel: 64 data bits.

## Slide 28
Scaling Out
The biggest models do not fit on one GPU
NVLink connects GPUs directly
Blackwell: 1.8 TB/s per GPU
Rubin: 3.6 TB/s per GPU
Rack-scale systems: 72 GPUs act as one
Now the interconnect is part of the architecture
Notes: NVLink 5 on Blackwell is 1.8 TB/s per GPU, NVLink 6 on Rubin 3.6 TB/s, per NVIDIA. The NVL72 racks connect 72 GPUs in one NVLink domain. For comparison, PCIe 5.0 x16 is about 64 GB/s each way. Model weights, activations and gradients are sharded across GPUs, so communication is constant.

## Slide 29
Using Tensor Cores
from PyTorch down to the hardware
Notes: Finally, connect the hardware back to the software from part 2. How does a line of PyTorch end up on these MAC arrays?

## Slide 30
PyTorch Mixed Precision
import torch
model = MyNet().cuda()
opt = torch.optim.AdamW(model.parameters())
for x, y in loader:
x, y = x.cuda(), y.cuda()
with torch.autocast("cuda", dtype=torch.bfloat16):
loss = loss_fn(model(x), y)
loss.backward()
opt.step()
opt.zero_grad()
Matrix multiplies in BF16 on tensor cores; weights kept in FP32
Notes: Inside the autocast block, PyTorch runs matrix multiplies and convolutions in BF16 and keeps sensitive operations such as reductions in FP32. The weights themselves stay FP32 in the optimizer. That one with-statement is what puts the work on tensor cores. MyNet, loader and loss_fn stand for any model, data loader and loss.

## Slide 31
Tensor Cores from CUDA: WMMA
#include <mma.h>
using namespace nvcuda;
__global__ void wmma_16x16(const half *a, const half *b, float *c)
{
wmma::fragment<wmma::matrix_a, 16, 16, 16, half, wmma::row_major> fa;
wmma::fragment<wmma::matrix_b, 16, 16, 16, half, wmma::row_major> fb;
wmma::fragment<wmma::accumulator, 16, 16, 16, float> fc;
wmma::fill_fragment(fc, 0.0f);
wmma::load_matrix_sync(fa, a, 16);
wmma::load_matrix_sync(fb, b, 16);
wmma::mma_sync(fc, fa, fb, fc); // D = A x B + C
wmma::store_matrix_sync(c, fc, 16, wmma::mem_row_major);
}
wmma_16x16<<<1, 32>>>(d_a, d_b, d_c); // one warp
Notes: WMMA, warp matrix multiply-accumulate, is the CUDA C++ API for tensor cores. The whole warp cooperates on one 16 x 16 x 16 tile: fragments are spread across the 32 threads' registers. FP16 in, FP32 accumulate. cuBLAS and CUTLASS use the lower-level mma and, on Hopper, wgmma instructions, but the idea is identical.

## Slide 32
One Operation, Four Levels
PyTorch
c = a @ b
cuBLAS / CUTLASS
tiled GEMM kernel
CUDA WMMA / mma
mma_sync( D, A, B, C )
Hardware
array of MACs: acc <= acc + a × b
You wrote the bottom level yourself
Notes: This is the summary of the whole three-session unit in one picture. Every level is the same multiply-accumulate. The higher you go, the less you control and the more you get for free.

## Slide 33
Key Ideas from Part 3
AI is mostly matrix multiply, which is mostly MAC
Tensor cores: a whole matrix operation per instruction
Fewer bits → smaller multipliers, less bandwidth
Systolic arrays reuse each value across a row or column
Bandwidth and interconnect matter as much as ALUs
Notes: Recap of part 3.

## Slide 34
The Whole Story
Part 1 throughput beats latency for parallel work
Part 2 CUDA: write it for one thread,
run it on millions
Part 3 the AI GPU is a sea of MACs,
fed by very wide memory
Every level of it starts as an HDL description
Notes: Close the unit. The same design moves recur: replicate a small module, amortize control, keep data close, and shrink the numbers when the application allows.

## Slide 35
Let's Build an Array
Exercise: 4 × 4 Systolic Matrix Multiply
1. Type in pe and systolic with N = 4
2. Write a testbench that skews the rows of A
and the columns of B as on the timing slide
3. Compare c_out with a software matrix multiply
for 20 random signed 8-bit matrices
4. Count the cycles. Do you get 3N − 2 ?
5. Set N = 8. What changes in your RTL? ( nothing! )
Notes: Step 2 is where students struggle: a shift register per row, of depth r, is the cleanest way to build the skew. Ask the strongest students to make it weight stationary, or to stream a second matrix in right behind the first.